Phys 319 Project Notes

How to attach things to the servo arm: you can often use hot glue. There are also special small screws that you can use. [https://forum.arduino.cc/index.php?topic=127745.0]
How they work: https://www.jameco.com/Jameco/workshop/howitworks/how-servo-motors-work.html
Servo wire colour meanings: / Red: Positive / Black (Or the darker of the remaining two.): Ground / White (or Yellow or Brown or the lighter of the remaining two): Signal / [https://www.rcgroups.com/forums/showthread.php?15071-What-are-the-three-servo-wires-for]
SPECIFICATIONS / Control system: Pulse width control, 1.52ms neutral Motor: 3-pole Power requirement: 4.8V or 6V (from receiver) Power consumption: 6V 8mA (at idle) Torque: 33 oz-in (2.4 kg-cm) @ 4.8V 42 oz-in (3.0 kg-cm) @ 6V Transit Time: 0.28 sec/60° @ 4.8V 0.22 sec/60° @ 6V Dimensions: 1.6 x 0.8 x 1.4" (1-9/16 x 13/16 x 1-7/16") (40 x 20 x 36mm) Weight: 1.6oz (1-9/16oz) (44g) Mounting on-center dimensions Width: .4" Length: 1.9" Shaft Diameter: 5.88mm / [https://www.towerhobbies.com/cgi-bin/wti0001p?&I=LXH318] / Pulse width range: 550-2330 µs / [https://servodatabase.com/servo/futaba/s148] / Also, (mostly useless): [https://futabausa.com/wp-content/uploads/2019/02/S148.pdf]
Compilation Setup: / export PATH=$PATH:$HOME/ti/msp430_gcc/bin / export INSTALL_DIR=$HOME/ti/msp430_gcc / export SUPPORT_FILE_DIRECTORY=$INSTALL_DIR/include / export DEVICE=msp430g2553 / export CFLAGS="-I $SUPPORT_FILE_DIRECTORY -mmcu=$DEVICE -Os -g" / export LFLAGS="-L $SUPPORT_FILE_DIRECTORY -T $DEVICE.ld" / export GCC_DIR=$INSTALL_DIR/bin / export CC=$GCC_DIR/msp430-elf-gcc
To Compile: $CC $CFLAGS $LFLAGS servo_drive.c -o servo_drive.elf
Getting servo to work: servo driver in “servo_drive.c” / Some experimentation showed that a good frequency to drive the servo at is with a period of 10 ms, i.e. a frequency of 100 Hz
Hall effect sensors: A1302 / Data sheet: http://www.learningaboutelectronics.com/Datasheets/A1302-hall-effector-sensor-datasheet.pdf / Field response: 2.5 mV/G / Hall effect stuff: http://www.learningaboutelectronics.com/Articles/Hall-effect-sensor-circuit.php
How to know what functions various pins can do? This page! / http://www.ti.com/lit/ds/symlink/msp430g2553.pdf
Useful ADC stuff: / Chapter 22, esp 22.3 -> registers
To get magic pwm constants, use determine_servo_angle.c / Azimuth magic numbers: / 1170, 550 / Altitude magic numbers: / 1325, 900